In this document I will draw up some conclusions of the assessment of the PitchYinFFT algorithm from Essentia, used in Freesound to estimate the pitch of an uploaded sound.

Method
The pitch estimation is assessed in two different manners: one uses the data already calculated by the Freesound extractor; the second will be to calculate the data by using the real sound. In the second method sounds that are not from Freesound can also be used to assess the pitch estimation. The following sounds are used: from Freesound the packs of the users 'Carlos Vaquero' (565 sounds) and 'Modular Samples' ($MODSMPL_SNDS$) and the soundpacks containing the tags 'good-sounds' (145 samples) are used. Of these sounds the descriptor files and soundfiles are downloaded. These add up to $AMOUNT_OF_FRSND_SNDS$ sounds. There are also some non-Freesound sounds used in this assessment. The sources of these sounds mentioned in the masterthesis of Carlos Vaquero [$ref$]. Two sound packs, namely guitar and violin from the philharmonia library (1608 sounds) and the piano pack from the IOWA library (225 sounds) are used.
First the correnctness of the estimates is considered, secondly factors that are able to predict the correctness of the estimate are investigated and lastly some improvements to the pitch estimation algorithm are proposed and assessed.

Results:
The overall mean of the raw error (calculated by subtracting the annotated pitch from the estimated pitch) in Hertz is: -70.3 for the Freesounddata and -129Hz for the audiofiles, making a total of: -122Hz. The mean errors per pack can be seen in table 1. The percentage of sounds that are estimated to have higher pitch than the annotated pitch is: 49% (see table 2). The mean of the absolute errors for the Freesounddata is: 309Hz, 173Hz for the soundfiles and 212Hz for the total. Because the pitch estimation is trying to estimate perceptual judgements it is usefull to take into account that the human pitch perception scale is not linear but a logarithmic scale. Therefore it might be more usefull to calculate the ammount of Equivalent Rectangular Bandwidths (ERB) bewteen the annotated sound and the estimated sound. The mean amount of ERB's between the estimated and the annotated pitch is: 7.34 for the Freesounddata, 4.46 for the soundfiles and in total the mean distance is 5.28 ERB's. See table 3;
The pitch estimation algorithm also gives a confidence measurement, ideally this would be a predictor for the estimation errors. The mean confidence is: 0.93 out of 1. Freesound however does not report the picht estimation confidence measurements, instead it supplies a pitch salience measurement, which will indicate how much tonal information the signal contains. In theory this could also be a predictor for the succes of the pitch estimation algorithm, as it is designed to deal with highly tonal signals. The mean pitch salience for the Freesounddata is: 0.47 out of 1, for the soundfiles it is 0.38 out of 1 and in total a mean salience of 0.41 out of one is found.
In tables 1 the calculated values per pack can be found.

Table 1: Mean errors per pack

Table 2: Mean absolute error and ERB distance per pack
Discussion:
The percentage of sounds that are estimated higher than the annotated pitch would indicate that the algorithm has a tendency to estimate the pitches to high. However when taking the mean of the errors into account indicates that especially high-annotated sounds are troublesome for the pitch estimation algorithm.

Performance:
0.8343472157229761 ~= 83.4% estimation and annotation fall in same ERB.

Estimated pitches versus annotated pitches:
- The mean of the error (estimated pitch – annotated pitch) is below zero:
  - mean error:	-109 Hz
    - excluding modularsamples:	-92.5Hz
  - and for ERB distances:	2.20 ERB's
    - ex. Modularsamples:	1.40 ERB's

Mean of annotated pitches is higher for wrongly estimated pitches:
  - In [26]: e, i = pTags_vs_err(d, 'ERBdist', 2)
  - mean pTag of err < 2:	625Hz
    - ex. modularsamples:	631Hz
  - mean pTag of err >= 2:	675Hz
    - ex. modularsamples:	951Hz
  - In [27]: e, i = pTags_vs_err(d, 'ERBdist')
  - mean pTag of err < mean:	612.2Hz
    - ex. modularsamples	631Hz
  - mean pTag of err >= mean:	716.7Hz
    - ex. modularsamples	974Hz
  - In [28]: e, i = pTags_vs_err(d, 'err')
  - mean pTag of err < mean:	576.2Hz
    - ex. modularsamples	617Hz
  - mean pTag of err >= mean:	888.5Hz
    - ex. modularsamples	1130Hz

- And the maximum value of the annotated pitches are also significantly higher for the wronly estimated pitches:
  - Low error:	27.5Hz	3.72 * 103Hz
  - High error:	24.4Hz	7.90 * 103Hz
- However: the standard deviations are lower for the wrongly extimated pitches than for the correctly estimated pitches:
  - In [26]: e, i = pTags_vs_err(d, 'ERBdist', 2):
  - standard deviation pTag of err < 2:	831Hz
    - ex. modularsamples:	1.09 * 103Hz
  - standard deviation pTag of err >= 2:	602Hz
    - ex. modularsamples	605Hz
  - In [27]: e, i = pTags_vs_err(d, 'ERBdist'):
  - standard deviation pTag of err < 2:	854Hz
    - ex. modularsamples:	1.11 * 103Hz
  - standard deviation pTag of err >= 2:	599Hz
    - ex. modularsamples:	605Hz
  - In [28]: e, i = pTags_vs_err(d, 'err'):
  - standard deviation pTag of err < 2:	918Hz
    - ex. modularsamples:	1.15 * 103Hz
  - standard deviation pTag of err >= 2:	585Hz
    - ex. modularsamples:	601Hz
  This suggest a possible improvement for the pitchYinFFT algorithm for high pitched sounds.
Confidence:
Mean of annotated pitches of estimations with high confidence are also higher:
  - In [29]: e, i = pTags_vs_err(d, 'conf')
  - mean pTag of conf < mean:	514Hz
    - ex modular samples;	596Hz
  - mean pTag of conf >= mean:	673Hz
    - ex modular samples:	1.13 * 103Hz
  - min, max pTag of conf < mean:	27.5	5.27 * 103Hz
  - min, max pTag of conf >= mean:	24.4	7.90 * 103Hz
  - standard deviation pTag conf < mean:	679Hz
    - ex. modularsamples:	702Hz
  - standard deviation pTag conf >= mean:	668Hz
    - ex. modularsamples:	780Hz
- But confidence is able to predict the correctness of the estimations:
  - include ERB distance < mean ERB distance, exclude otherwise:
    - 76.9% correct
    - ex. modularsamples: 84.4% correct
  - include error < mean error, exclude otherwise:
    - 75.7% correct
    - ex. modularsamples: 83.15 correct
But there is no confidence measure in the Freesound data!?

- Salience is not a good predictor for the correctness of the estimations:
  - include ERB distance < mean ERB distance, exclude otherwise:
    - 54.1% correct
    - ex. modularsamples: 54.8% correct
  - include error < mean error, exclude otherwise:
    - 53.2% correct
    - ex. modularsamples: 54.3% correct
This poses a requirement of the algorithm for the Freesound extraction?